## Slide 1: Distributed Multi-Sensor Control for Multi-Target Tracking
22/11/2022
Aidan Blair, Amirali Khodadadian Gostar, Ruwan Tennakoon, Alireza Bab-Hadiashar, Xiaodong Li, Jennifer Palmer and Reza Hoseinnezhad
RMIT University, Melbourne, Australia

## Slide 2: Multi-Sensor, Multi-Target Tracking Background
Aim is to track the states of multiple targets using multiple sensors with limited FoV.
Many domains: Autonomous cars, drones, on water/underwater vehicles, satellites.

## Slide 3: Multi-Sensor Control Background
Aim to move the sensors in a way that they get the best measurements to accurately track the targets.
Quality of actions is measured either by information gain or optimizing a heuristic objective function.

## Slide 4: Problem Statement
To control a distributed & dynamic network of mobile sensors to accurately track a time-varying number of mobile targets.

## Slide 5: Problem Formulation
The problem has been formulated as a distributed multi-sensor control problem using RFS filters for multi-target tracking and distributed information fusion.

## Slide 6: LMB Filter
The Random Finite Set (RFS) framework for multi-target tracking is used, specifically the Labeled Multi-Bernoulli (LMB) filter.
LMB density: , each potential target is represented by a Bernoulli existence probability a spatial distribution , and a label .

## Slide 7: Prediction & Update Steps
The parameters for the next time step are predicted using the Chapman-Kolmogorov equation:
The parameters for the next time step are updated using the multi-object Bayes’ rule:

## Slide 8: Multi-Sensor Control Formulation
Each sensor has a number of possible sensor control commands .
A multi-sensor control command is formed as a tuple of single-sensor control commands, .

## Slide 9: Proposed Solution
Each sensor looks at local sensor neighborhood .
Sensors calculate best multi-sensor control command for neighborhood, using coordinate descent to quickly optimize solutions at each sensor.

## Slide 10: Proposed Solution
Each sensor communicates to neighbors the single-sensor control command they calculated for the neighbor, and the corresponding objective function value.
The sensor control command with the highest objective function value is chosen.

## Slide 11: Coordinate Descent
Similar to gradient descent, except only a single parameter is optimized at a time.
Suitable for optimizing a multi-sensor control command, as each single-sensor control command is discrete.

## Slide 12: Kullback-Leibler Divergence
The Kullback-Leibler Divergence (KLD) is a statistical measure for the difference between two distributions.[1]
denotes the set integral from FISST.[2]
[1] Kullback, S. & Leibler, R.A., On information and sufficiency, 1951.
[2] Mahler, R., Random-set approach to data fusion, 1994.

## Slide 13: Objective Function
The objective function used is the KLD between the local predicted density and the fusion of neighbourhood pseudo-updated densities.
Searches the possible control commands of a single sensor to find the command that maximizes the KLD, given the actions for the other sensors are fixed.
Cycle through each , repeat until convergence.

## Slide 14: Simulation Scenario

## Slide 15: Scenario Parameters
Used Distributed Complementary Fusion[3]
3 Possible Actions: Stationary, Rotate 22.5 deg Clockwise & Rotate 22.5 deg Anti-Clockwise
Accuracy measured by Optimal Sub-Pattern Assignment (OSPA) distance[4], composed of localization and cardinality errors.
Use a particle filter approximation for LMB densities
[4] Schuhmacher, D., Vo, B.-T. & Vo, B.-N., A consistent metric for performance evaluation of multi-object filters, 2008.
[3] Klupacs, J. et al., Distributed Complementary Fusion for Connected Vehicles, 2022.

## Slide 16: Scenario Results

## Slide 17: Scenario Results - OSPA
 | OSPA Distance | OSPA Localization | OSPA Cardinality
Fixed w/ fusion | 27.0212 | 6.3738 | 20.6478
Independent Multi-Sensor Control w/ fusion | 76.9432 | 1.3996 | 75.5436
Independent Multi-Sensor Control w/o fusion | 16.2745 | 5.6233 | 10.6512
Multi-Sensor Control with fusion | 11.3912 | 4.7822 | 6.6090

## Slide 18: Conclusion
A sensor control algorithm for a distributed & dynamic sensor of networks for RFS based multi-target tracking applications has been developed.
Areas to explore further: computationally cheaper methods and more complicated scenarios.

## Slide 19: Thank you for listening!

## Slide 20: Target Measurements
Each sensor partially observes the multi-target state , returning a measurement set .
Observation depends on sensor FoV and detection probability .

## Slide 21: Distributed & Dynamic Sensor Network

## Slide 22: Contents
Background
Problem Statement
Problem Formulation
Proposed Solution
Results
Conclusion